## Slide 1
JLab “SciPhi-XVI” KNL Cluster
Thomas Jefferson National Accelerator Facility
Sandy.Philpott@jlab.org
IXPUG @ TACC 09/26/17

## Slide 2: Background
The DOE USQCD project’s FY16 procurement was installed at JLab in August 2016
3 racks of 64 7230 KNL nodes, ~ $ 1M
In FY17 (October 3!), exercised the upgrade option in the award, for a 4th rack, ~ $ 0.25M, installed late October
Competitive procurement…
  Intel Xeon Phi / Knights Landing
  NVIDIA Pascal GPU, CUDA
  Intel Broadwell CPU server
Consideration factors
  hardware availability timeline
  high speed network – 100 Gbps price/performance; Omni-Path or Infiniband
  available configurations
  reflective benchmarks of USQCD codes
Strategy: optimize portfolio of machines to get the most science on the portfolio of applications
KNL proposals achieved highest aggregate score on all performance metrics and sub-metrics

## Slide 3: Since install
4th rack of 64 nodes installed, for a total of 264 nodes
  and more temp location power circuits
Top500 #397! Green500 #10!
Relocation into new Hot Aisle Containment System last December
MCDRAM flat/cache reboots (sometimes hung?)
  daemon to switch not yet automated…
Multi-node job insight
  Reboot/power cycle between every job?
Early-ship KNL silicon … 26 nodes replaced as we discovered issues
User benchmarks … are sometimes hard to get ...
Testbed configured in June; one rack production in July
  Xppsl 1.5.1, OPA 10.3
  New production BIOS, along with chip screening
    R01.02.0072

## Slide 4: Top500 #397 on Nov ‘16 list

## Slide 5: Green500 #10 on Nov ‘16 list

## Slide 6: KNL Cluster Hardware
264 Intel Xeon Phi 7230
64 cores, 1.3GHz, 256 threads, 192GB RAM, 16GB MCDRAM
1 TB Seagate disk
Intel Omni-Path 100gbps
Total: 16,896 cores, >50 TB memory
Server Board:
Intel S7200AP
BIOS: S72C610.86B.01.01.0190.080520162104 (08/05/2016)

## Slide 7: KNL Cluster Software
CentOS 7.2:
3.10.0-327.22.2.el7.xppsl_1.4.1.3272.x86_64
openMPI:
  openmpi-1.10.0-10.el7.x86_64
  openmpi_intel_hfi-1.10.2-8.x86_64
  openmpi_gcc-1.10.2-8.x86_64
  openmpi_gcc_hfi-1.10.2-8.x86_64
  openmpi_pgi_hfi-1.10.2-8.x86_64
Mvapich2
  mvapich2_gcc_hfi-2.1-4.x86_64
  mvapich2_pgi_hfi-2.1-4.x86_64
  mvapich2_intel_hfi-2.1-4.x86_64
  mvapich2_gcc-2.1-4.x86_64
Intel Parallel Studio
  parallel_studio_xe_2016.3.067
  parallel_studio_xe_2017

## Slide 8: Memory options
Changing nodes with reboot to update BIOS to set MCDRAM to Flat or Cache mode per user job tag…
latest version of syscfg
(hwloc_dump_hwdata showed different settings?!)
Works … but nodes would often randomly hang during the process, remaining down until a required a power cycle ...
Turns out, Intel requires a CPU reset (IPMI “power cycle”) power cycle anyway to guarantee the memory setting
New solution in the works ...
Update the BIOS, check the chip set; if “old” – update ...
But this takes several hours of manual intervention on each node! Final arrangements await ...

## Slide 9: Omni-Path
Spine : 4 64 port switches; Leaf switch uplinks in bundles of 6,6,4
for 256 nodes, 2 core switches consumed, 3rd support s 4 links to the file system plus 8 additional nodes with a little room to spare
32 nodes connect to a 48 port leaf switch
- nominally 2:1 oversubscribed, but effectively full bandwidth per node
Need more than a single core to drive OPA to full bandwidth
/dev/hfi1 driver – use the correct one, or
  hfi_userinit: PSM2 and driver version mismatch Driver initialization failure on /dev/hfi1 (err=23) [3] MPI startup(): tmi fabric is not available and fallback fabric is not enabled
Managed OPA switch subnet manager stopped running several times; recommended for <100 nodes
so, installed subnet manager on 2 hosts

## Slide 10: Adding OPA to the Fabric

## Slide 11: OPA to IB File Systems
Omni-Path 16p nodes need to reach Lustre and NFS file services on the Infiniband QDR fabric…
Lustre: /cache (on tape), /volatile (scratch)
Use 4 LNet routers between OPA and IB
NFS : /home, /dist, /work
Use 2 JLab hosts with IB and OPA connections, with IP routing

## Slide 12: Observations
Double check the power
  Our first HPL run tripped the single power panel
  PDU reached >100 KW, can run at 135KW, 90% of rating, when nodes distributed across 2 panels
5 nodes of 200 initially had hardware errors
  3 MCDRAM
  1 bad DIMM slot
  1 won’t POST
Transparent khugepaged problematic
  – turned off; watching …

## Slide 13: Updates to PBS/Torque
prologue
sync; echo 3 > /proc/sys/vm/drop_caches
But, still problematic … must do it on every node in the job!
prologue.parallel
config
  Increase alarm timeout to execute the job prologue to 5 minutes
  our setting of 1 minute was leaving many jobs orphaned, nodes “busy”, required manual intervention
  $ prologalarm 300

## Slide 14: Still To Do…
Benchmark users’ USQCD codes relative to conventional cores
  Currently assuming 3 Jpsi core hour, the reference for USQCD
Bin nodes into fast/medium/slow, with 80% in medium, so jobs land on consistently performant nodes (we’ve seen >10% spread) ?
Automate cache/flat memory reboots based on job demands
  PBS/Torque/Maui
Chip screening, BIOS updates for 3 more racks
  More spares on hand by vendor, to keep downtime < 0.5%
Investigate Zonesort kernel module, Intel Cluster Checker tool
More sharing experiences with other KNL sites

## Slide 15: We want to share expertise!
  Fall16 HEPiX HPC BOF
  Procurements
  Allocations
  Benchmarks
  Software
  Porting
  Lessons learned
  NLCIO group brown bag lunches?
  IXPUG