## Slide 1: Next-Gen Accleration with Multi-Hybrid Devices - Is GPU Enough ? -
Taisuke Boku
Director, Center for Computational Sciences
University of Tsukuba
taisuke@ccs.tsukuba.ac.jp

## Slide 2: (before starting) Introduction of our new supercomputer Pegasus
CCS (Center for Computational Sciences), University of Tsukuba
Intel SPR + Intel Optane + NVIDIA H100
#190 in TOP500 (3.48PF, 53.5%)
#12 in Green500 (40.5 GF/W, 78.4kW)

## Slide 3: Pegasus: world first combination of H100+SPR+PMEM+NDR200
total Performance
  120 nodes, 6.5 PFlops, 240 TiB (PMEM)
node components
  NVIDIA H100 PCIe (gen5)
  Intel Sapphire Rapids (SPR)
  Intel Optane ver3
Interconnection Network
  NDR200: NVIDIA Quantum-2 IB with 200Gbops full bisection b/w
parallel file system (DDN)
  7.1 PByte, 40 GB/s
SPR
CPU
H100 GPU
DRAM 128 GB
PMEM 2 TB
200Gbps full bisection
120 nodes
NVMe SSD 6.4 TB
HPL: 3.48 PF (54%)
MPI pingpoing: 23.9MB/s (95.7%)

## Slide 4: Pegasus outlook
computation nodes (120)
IB switch +login server
file server
Pegasus at CCS, Univ. of Tsukuba (2022/12~)

## Slide 5: Computation node
CPU (SPR)
DRAM and PMEM
GPU (H100)
Network (IB NDR)
SSD

## Slide 6: How to use GPU + Big Memory (PMEM) for HPC/BD/AI ?
GPU
  totally important for both HPC and AI
  powerful GPU contributes HPC ↔ AI coupling
Ultra large capacity of medium~high speed memory
  astrophysics, climate, life science: requiring large capacity of working set with relatively low FLOPS requirement
In-Situ processing
  bypassing the slow in/out of large capacity of file data ⇨ PMEM technology support
High-speed distributed storage
  even as a distributed storage, much faster solution is possible (shown later)

## Slide 7: Accelerators in HPC ⇒ majority = GPU
Is GPU perfect ?
  good for many applications (replacing vector machines)
  depending on very wide and regular parallelism
    large scale SIMD (STMD) mechanism in a chip
    high bandwidth memory (HBM, HBM2) and local memory
  insufficient for cases with...
    not enough parallelism
    not regular computation (warp divergence)
    frequent inter-node communication (kernel switch, go back to CPU)
NVIDIA Tesla H100 Hopper Architecture GPU (from NVIDIA web page)

## Slide 8: FPGA in HPC
Goodness of recent FPGA for HPC
  True codesigning with applications (essential)
  Programmability improvement: OpenCL, other high level languages
  High performance interconnect: 100Gbps x 4
  Precision control is possible
  Relatively low power
Problems
  Programmability: OpenCL is not enough, not efficient
  Low standard FLOPS: still cannot catch up to GPU -> “never try what GPU works well on”
  Memory bandwidth: 1-gen older than high-end CPU/GPU -> be improved by HBM, but still difficult to use
BittWare 520N with Intel Stratix10 FPGA equipped with 4x 100Gbps optical interconnection interfaces

## Slide 9: GPU vs FPGA as HPC solutions
device | GPU | FPGA
parallelization | SIMD (x multi-group) | pipeline (x multi-group)
standard FLOPS | 😃😃 (>1000 cores) | 😃 (~100 pipeline)
conditional branch | 😢 (warp divergence) | 😃 (both direction)
memory | 😃😃 (HBM2e) | 😢 (DDR)→😃 (HBM2)
interconnect | 😢 (via host facility) | 😃😃 (own optical links)
programming | 😃 (CUDA, OpenACC, OpenMP) | 😢 (HDL)→😏 (HLS)
self-controllability | 😢 (slave device of host CPU) | 😃 (autonomous)
HPC applications | 😃 (various fields) | 😢 (limited)

## Slide 10: Coupling GPU and FPGA, why ?
Many multi-physical simulation to combine several sorts of different phenomena on a system is required in advanced physics
  space – particle reaction
  fluid dynamics with chemical reaction
  macroscopic/microscopic hybrid simulation molecular simulation
Characteristics and dynamism of parallelism drastically changes during the simulation
  SIMD friendly or pipeline friendly
  small fraction of low degree parallelism in a code makes “last one mile problem” under Amdahl‘s Law

## Slide 11: CHARM: Cooperative Heterogeneous Acceleration with Reconfigurable Multi-devices
CPU
GPU
FPGA
comp.
PCIe
comm.
invoke GPU/FPGA kernsls
data transfer via PCIe
(invoked from FPGA)
CPU
GPU
FPGA
comp.
PCIe
comm.
FPGA Network
Application oriented FPGA-FPGA communication
Basic cluster with GPUs (by InfiniBand)
100Gbps direct optical link
multi-physics/multi-scale
complicated problem
Cooperative computing with GPU and FPGA

## Slide 12: Cygnus: world first multi-hybrid cluster with GPU+FPGA
Cygnus supercomputer at Center for Computational Sciences, Univ. of Tsukuba (Apr. 2019~) 85 nodes in total including 32 “Albireo” nodes with GPU+FPGA (other “Deneb” nodes have GPU only)
@ CCS, Univ. of Tsukuba (deployed by NEC)

## Slide 13: Single node configuration (Albireo)
CPU:Xeon Gold
PCIe network (switch)
GPU
GPU
FPGA
IB EDR HCA
IB EDR HCA
Inter-FPGA direct network
(100Gbps x4)
IB network
(100Gbps x2)
CPU:Xeon Gold
PCIe network (switch)
GPU
GPU
FPGA
IB EDR HCA
IB EDR HCA
Inter-FPGA direct network
(100Gbps x4)
IB network
(100Gbps x2)
SINGLE
NODE
(with FPGA)
Each node is equipped with both IB EDR and FPGA-direct network
(32 nodes are equipped with both FPGAs and GPUs,
and other nodes are with GPUs only)
CPU
PCIe network (switch)
GPU
GPU
FPGA
HCA
HCA
Inter-FPGA direct network
(100Gbps x4)
Network switch
(100Gbps x2)
CPU
PCIe network (switch)
GPU
GPU
FPGA
HCA
HCA
Inter-FPGA direct network
(100Gbps x4)
SINGLE
NODE
(with FPGA)
Each node is equipped with both IB EDR and FPGA-direct network
(32 nodes are equipped with both FPGAs and GPUs,
and other nodes are with GPUs only)
Each node is equipped with both IB EDR and FPGA-direct network
Some nodes are equipped with both FPGAs and GPUs, and other nodes are with GPUs only
Network switch
(100Gbps x2)

## Slide 14: Two types of interconnection network
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA
comp. node
…
IB HDR100/200 Network (100Gbps x4/node)
For all computation nodes (Albireo and Deneb) are connected by full-bisection Fat Tree network with 4 channels of InfiniBand HDR100 (combined to HDR200 switch) for parallel processing communication such as MPI, and also used to access to Lustre shared file system.
comp. node
comp. node
…
comp. node
Deneb nodes
Albireo nodes
comp. node
comp. node
Inter-FPGA direct network
(only for Albireo nodes)
InfiniBand HDR100/200 network for parallel processing communication and shared file system access from all nodes
…
…
Inter-FPGA torus network
64 of FPGAs on Albireo nodes (2FPGAS/node) are connected by 8x8 2D torus network without switch

## Slide 15
GPU
GPU
GPU
GPU
FPGA
FPGA
CPU
CPU
IB HDR100 x4 ⇨ HDR200 x2
100Gbps x4
FPGA optical
network x2
IB HDR200 switch (for full-bisection Fat-Tree)
Albireo node
1.2Tbps/node

## Slide 16
King-Ghidorah (by Toho)

## Slide 17
King-Ghidorah (by Toho)
How to Attack ??
GPU
GPU
FPGA
CPU
IB HCA
IB HCA
Multi-Hetero Multi-Node
Optical Link

## Slide 18: Researches around Cygnus
FPGA-network: CIRCUS (Communication Integrated Reconfigurable CompUting System)
  direct interconnect facility among FPGA boards by multi-dimensional optical link (~100Gps) with router and OpenCL-ready API
  pipelining all computation and communication seamlessly
GPU-FPGA DMA: kicked by FPGA (without CPU)
  PCIe-protocol base DMA engine to reduce multi-device high speed data transfer
Programming:
  MHOAT (Multi-Hetero OpenACC Translator) ⇒ single code of OpenACC is broken into GPU kernels and FPGA kernels according to user description
  Intel oneAPI ⇒ task-by-task manner assignment of computation part to GPU and FPGA under DPC++ device queue management
Appllication: ARGOT, application on astrophysics for early-universe object generation
  two main parts are executed by GPU and FPGA

## Slide 19: CIRCUS
Intel FPGA SDK for OpenCL
  We can describe FPGA hardware in OpenCL
Problem: How to write inter-FPGA communication code in OpenCL?
  MPI is the standard method for HPC applications
  It is memory-to-memory communication, not suitable for FPGAs
  We need to utilize pipeline-based communication in an FPGA
→CIRCUS: Communication Integrated Reconfigurable CompUting System
  Pipelined communication and computation
    communicate from or to a computation pipeline directly
sender(__global float* restrict x, int n) {
for (int i = 0; i < n; i++) {
float v = x[i];
write_channel_intel(simple_out, v);
}
}
sender code on FPGA1
receiver(__global float* restrict x, int n) {
for (int i = 0; i < n; i++) {
float v = read_channel_intel(simple_in);
x[i] = v;
}
}
receiver code on FPGA2
Comm.
Backend
* N. Fujita, et al., “Performance Evaluation of Pipelined Communication Combined with Computation in OpenCL Programming on FPGA”, AsHES2020.
Notes: To solve programming problem, we introduce Channel over Ethernet, CoE for short, communication system.
Basic concept of CoE system is extending channels to external communications.
And using channels means pipeline manner communication, sending or receiving data from or to compute pipeline directly.
And also, multiple networking channels are supported.
In OpenCL, only one writing and reading point per channels is allowed.
So, some multiplexing logics are needed to achieve this.
These figures show example code using CoE.
Write_channel_intel and read_channel_intel are the standard APIs in Intel OpenCL.
After writing data into this channel, it is transferred to an FPGA in another node through the CoE backends.
I will talk about the backend in the next few slides.

## Slide 20: Router in CIRCUS
Router written in Verilog HDL and implemented in BSP
→ for non-neighbor FPGA comm.
packet queue and switching in CIRCUS router
QSFP28 x4

## Slide 21: CIRCUS performance
latency+ /hop ~250 ns
Latency（1hop~7hops）
max. throughput 90.2Gbps
min. latency 500ns
Throughput（1hop~7hops）
Better
Better
Evaluated on up to 8 Bittware 520N FPGA boards in Cygnus supercomputer at CCS, University of Tsukuba
N. Fujita, et al., “Performance Evaluation of Pipelined Communication Combined with Computation in OpenCL Programming on FPGA”, AsHES2020.
Notes: These figures show the result of the pingpong benchmark.
We used up to 8 FPGAs on the Cygnus system.
1-hop means communication between two neighboring FPGAs.
2-hops means communication to the neighbor of the neighbor FPGA.
The right figure shows the latency result.
The minimum latency is 500ns and each hops adds about 250ns.
The left figure shows the throughput result.
The maximum throughput is 90.2Gbps and the minimum latency is 500ns.
Because the larger hop case has larger communication latency, the throughput is less on the small and medium length messages.
However, the long message achieves the almost same performance.

## Slide 22: What CIRCUS provides ?
CIRCUS: Communication Integrated Reconfigurable CompUting System
  Goal1: providing High Level Synthesis programming environment for parallel FPGA system by FPGA-FPGA communication link
  Goal2: combining computation pipeline and communication pipeline seamlessly to fully utilize the goodness of FPGA computation/communication

## Slide 23: Current problem of CISCUS
There is no flow-control mechanism
  user should care on synchronization between FPGAs on algorithm level
  we can add buffer on the channel but it eliminates the goodness of “pure-pipelining” feature of CISCUS
Solution: importing another system ⇨ Kyokko (by Nagasaki U.)
  Kyokko has almost identical API with Intel SerialLight-3 used in CIRCUS
  we already implemented Intel Stratix10 H-Tile (up to 100Gbps/link) from original Xilinx implementation and Intel Stratix10 L-Tile (up to 10Gbps/link) ⇨ ongoing work (within a couple of months, hopefully)
Item | Performance
bandwidth / link | 99.985 [Gbps] (99.985% of peak)
latency / hop | 181.8 [nsec]
flow control overhead (XON or XOFF) | 1.7 [packet]
Preliminary evaluation shows enough performance to replace SerialLight-3 to Kyokko on CIRCUS

## Slide 24: Bandwidth of GPU-FPGA DMA
Data size: 4 ~ 2G Bytes (PCIe gen3x8*: 7.8GB/s peak) * due to Intel FPGA BSP limitation
Up to 7.2 GB/s (FPGA → GPU)
Up to 3.7 GB/s (GPU → FPGA)
Higher is Better

## Slide 25: Programming in CHARM (history)
Gen-1: low level naive coding
  compile code fraction with separate compiler for GPU (with CPU) and FPGA
  GPU+CPU: CUDA or OpenACC (PGI Compiler/NVHPC)
  FPGA: OpenCL (Intel FPGA SDK for OpenCL)
  merging partial objects in one (removing symbol conflicts)
Gen-2: oneAPI
  DPC++ or multi-language (CUDA for GPU and OpenCL for FPGA)
  test code works well, but some problem for practical codes
Gen-3: MHOAT
  OpenACC-only coding with several backend compilers (PGI/NVHPC and OpenARC)
  meta-compiler for code separation from a single code of OpenACC
  still kernel-level optimization for each device is required

## Slide 26: Possible coding method for CHARM: oneAPI
oneAPI is a cross-architecture programming framework
  simplify the development across different architectures
Data Pallalell C++ (DPC++)
  DPC++ = C++ + SYCL + extensions
  enables unified description across different architectures
Notes: oneAPI is a cross-architecture programming framework proposed by Intel. The purpose of oneAPI is to simplify the development across different architectures.
oneAPI includes the Data Pallalell C++ programming language and a set of libraries enablering development in a single languarge and API.
DPC++ is based on C++, SYCL specification, and extension.
SYCL is a standard that provides an abstract layer and unifies the development environment of different accelerators.
DPC++ enables unified description across different architectures

## Slide 27: CHARM by oneAPI
In oneAPI, programming in DPC++ is recommended
  (a) approach
  Problem: Existing GPU and FPGA code is written in other languages such as CUDA, OpenCL, etc
    These code assets already exist
  Reimplementation by DPC++ is a burden for users
oneAPI also can use modules written in other languages
  (b) approach
  Code can be reused

## Slide 28: How much easier to program using oneAPI?
cudaMemcpy(…); // Call the CUDA kernel gpu_kernel<<<grid, block>>>(…); cudaMemcpy(…); clEnqueueWriteBuffer(…); clSetKernelArg(…); // Call the OpenCL kernel clEnqueueTask(…, fpga_kernel,…); clEnqueueReadBuffer(…);
gpu_queue.memcpy(…); gpu_queue.submit([&](handler& h) { h.interop_task([=](interop_handler ih) { // Call the CUDA kernel gpu_kernel<<<grid, block>>>(…); }); }); gpu_queue.memcpy(…); fpga_queue.memcpy(…); fpga_queue.submit([&](sycl::handler &h) { // Call the OpenCL kernel h.set_args(…); h.single_task(fpga_kernel); }); fpga_queue.memcpy(…);
CUDA + OpenCL programming model
oneAPI calling CUDA+OpenCL kernels
CUDA API
OpenCL API
using oneAPI, we can control GPU and FPGA in a single manner of invocation kernels

## Slide 29: oneAPI is good, but not perfect especially for FPGA
There are some multi-device supporting environment
  oneAPI, OpenARC (ORNL), ...
Most of them focus on the dynamic load balancing
  prepare binary for all devices such as GPU, FPGA, many-core
  FPGA is quite expensive to include all kernels because it impliments all the code into logic circuit although they might not be used
  CPU and GPU is easy to hold entire code (thanks to ISA) but FPGA is not
  it is not practical to do “run time compilation” on FPGA
  current oneAPI is not ready for dynamic reconfiguration on FPGA
We need to separate kernels according to their functionality
In most of code, performance characteristics differ on GPU and FPGA
  it may not work well even considering load balancing on them
  against to CHARM concept

## Slide 30: New method: Unified OpenACC meta-compiler
OpenACC is available both for GPU and FPGA
  under development in collaboration between CCS-Tsukuba and FTG-ORNL
  GPU compilation – PGI OpenACC compiler
  FPGA compilation – OpenARC for FPGA on OpenACC, developed at ORNL -> collaboration between CCS and ORNL (Jeff Vetter, Seyong Lee, etc.)
Solving some conflict on host code environment and run-time
  Basic running is confirmed and testing example codes
Issues
  Performance enhancement on GPU and FPGA totally differs
    GPU – horizontal (data) parallelism in SIMD manner
    FPGA – clock level pipelining
    Memory model difference: HBM2 vs BRAM
⇒ MHOAT (Multi-Hybrid OpenACC Translator)

## Slide 31: MHOAT (Multi-Hybrid OpenACC Translator)
User describes the code in OpenACC (currently C only)
  considering the part to be offloaded to certain type of accelerator (GPU or FPGA) ⇨ introducing extended directive #pragma accomn target_dev(device)
  data directive is treated according to the mapped device
MHOAT separates the code block (task) to “host”, “GPU” and “FPGA” execution
Each block is compiled by back-end, then assembled for single executable and bit-stream for FPGA

## Slide 32: Compilation flow of MHOAT
Backend (existing compilers)
fpga.o
gpu.o
a.out
Executable
fpga .cpp
Intel FPGA SDK for OpenCL
fpga.cl
fpga .aocx
fpga .aoco
OpenCL kernel
OpenCL host
OpenACC
Object Files
transfer FPGA binary & run-time
PGI Compiler (pgc++ -c)
gpu.c
fpga.c
aoc -c
pgc++
aoc
pgc++ -c
OpenARC
single program
int main() {
~~~~~~~~~~
#pragma accomn targetdev (GPU)
~~~~~~~~~~
~~~~~~~~~~
#pragma accomn targetdev (FPGA)
~~~~~~~~~~
~~~~~~~~~~
~~~~~~~~~~
return 0;
}
openacc.c
M
H
O
A
T

## Slide 33: Application Example – ARGOT code
ARGOT (Accelerated Radiative transfer on Grids using Oct-Tree)
  Simulator for early stage universe where the first stars and galaxies were born
  Radiative transfer code developed in Center for Computational Sciences (CCS), University of Tsukuba
  CPU (OpenMP) and GPU (CUDA) implementations are available
  Inter-node parallelisms is also supported using MPI
ART (Authentic Radiation Transfer) method
  It solves radiative transfer from light source spreading out in the space
  Dominant computation part (90%~) of the ARGOT code

## Slide 34: Cosmic Radiative Transfer Simulation ARGOT *
Point Source
Diffuse Photon
Two computation elements in ARGOT code: ARGOT method and ART method
ARGOT method: Point Source processing
ART method (Authentic Radiation Transfer): Diffused Photon processing

## Slide 35: Cosmic Radiative Transfer Simulation ARGOT *
GPU acceleration
ARGOT method
for radiative transfer (RT)
from point source
ARGOT (Accelerated Radiative transfer on Grids using Oct-Tree) code
Point Source
ART method
for RT from matters
spatially spreading out
FPGA acceleration
Diffuse Photon
FPGA
GPU
GPU
GPU
FPGA
FPGA
CHARM
Two computation elements in ARGOT code: ARGOT method and ART method
ARGOT method: Point Source processing
ART method (Authentic Radiation Transfer): Diffused Photon processing

## Slide 36: ARGOT method
is to solve the radiative transfer from point radiation sources
builds an oct-tree data structure for the distribution of radiation sources
  It's a 3-dimensional problem space, so it's an octave tree
  For point of view from the target mesh , it is treated as a same light source if the light sources fall within a certain degree
is similar to Tree-Code in gravity calculation
  suitable for the GPU
  Each ray is assigned to each CUDA thread, and then these computations are conducted in parallel
effective number of sources : Ns ➡ log Ns
Notes: First, I am going to talk about the ARGOT method.
To solve the radiative transfer from point radiation sources, it is necessary to compute the optical depth between each pair of point radiation sources and the target mesh grid.
Assuming that the number of mesh grids is constant, the computational complexity is proportional to the number of point radiation sources.
To address this, the ARGOT method builds an oct-tree data structure for the distribution of radiation sources, as shown here.
For point of view from the target mesh , it is treated as a same light source if the light sources fall within a certain degree.
That’s why the effective number of sources is reduced from N to the logarithm of N.
As you can see, this method is similar to Tree-Code in gravity calculation, which means it’s suitable for the GPU.
So, each ray is assigned to each CUDA thread, and then these computations are conducted in parallel.

## Slide 37: ART Method
ART method is based on ray-tracing method
  3D target space split into 3D meshes
  Rays come from boundaries and move in straight in parallel with each other
  Directions (angles) are given by HEALPix algorithm
ART method computes radiative intensity on each mesh as shows as formula (1)
  Bottleneck of this kernel is the exponential function (expf)
  There is one expf call per frequency (ν). Number of frequency is from 1 to 6 at maximum, depending on the target problem
  All computation uses single precision computations
Memory access pattern for mesh data is varies depending on ray’s direction with short vectors
  Not suitable for GPU’s HBM
  FPGAs can optimize it using BRAM (Block RAM = SRAM)
  Multiple pipelines on FPGA work well
Notes: ART method is based on ray-tracing method.
It split the target 3D space into 3D meshes, and the typical size of meshes will be between 100 cued to 1000 cubed.
Ray for ray tracing comes from boundaries and they are move in straight in parallel with each other.
Memory access pattern for mesh data is varies depending on ray direction.
In some cases, memory access will be consecutive, but in the other cases, it will be scattered.
Therefore, we consider ART method is not suitable for SIMD architecture.
On the other hand, FPGAs can handle this well because we can make custom memory access logics on an FPGA.

## Slide 38: FPGA implementation of ART method
Domain Decomposition + Intel Channel for multi-FPGA expansion
Comm. path of ray data (Intel Channel)
x
y
z
Mesh reader
&
Mesh
writer
FPGA
Comp. engine
for ART method
cores (OpenCL kernels)
External memory (DRAM)
load mesh data into comp. engine
store comp. result (mesh data) in DRAM

## Slide 39: Parallel ART with multiple FPGAs
replacing Intel Channel at FPGA border with CIRCUS
  making cluster of ART execution kernels with Intel Channel or CIRCUS
Intel Channel
CIRCUS Channel

## Slide 40: Version history of ARGOT code
All in CPU : OpenMP
All in GPU : CUDA
ARGOT method in GPU : CUDA ART method in FPGA: OpenCL
naive program (CUDA+ OpenCL kernel)
ARGOT method in GPU : CUDA ART method in FPGA: OpenCL
oneAPI assembling
All in GPU : OpenACC
ARGOT method in GPU : OpenACC ART method in FPGA: OpenACC
MHOAT
CHARM
all accelerated version implies some fraction of
CPU computing with OpenMP

## Slide 41: Evaluation Environment
PPX (Pre PACS-X) mini cluster which is the prototype of Cygnus
A computation node of PPX
Hardware specification | 
CPU | Intel Xeon E5-2690 v4 x2
Host Memory | DDR4-2400 8GB x8
GPU | NVIDIA Tesla P100 (PCIe Gen3 x16)
GPU Memory | 16 GiB CoWoS HBM2 @ 720 GB/s with ECC
FPGA | BittWare 520N (1SG280HN2F43E2VG) equipped with 100Gbps x 4 chan.
FPGA Memory | DDR4 2400MHz 32 GB (8GB × 4)
InfiniBand | Mellanox ConnectX-4 Singleport EDR MCX455A-ECAT
Software specification | 
OS | CentOS 7.9
Host Compiler | gcc 4.8.5
GPU Compiler | CUDA 11.2.152
Open MPI | 3.1.0
OpenCL SDK | Intel FPGA SDK for OpenCL 19.4.0 Build 64 Pro Edition
PCIe for FPGA is just gen3 x 8 lanes, but does not affect on performance because the communication overhead is ~1%
Notes: Now, it’s time to talk about performance evaluation.
This slide shows our evaluation testbed called Pre-PACS-X, which is working at Center for Computational Sciences, University of Tsukuba.
This is not ‘X’, this is Roman numerals, OK.
This is a heterogeneous platform composed of three kinds of devices: two Intel Xeon E5-2660 v4 CPUs, two PCIe-based NVIDIA P100 GPUs, and a single BittWare A10PL4 FPGA board.
In this evaluation, we used a single GPU and an FPGA as surrounded by the red line, as shown here.

## Slide 42: Performance evaluation (bare CUDA+OpenCL vs with oneAPI)
Problem size of
Single node (1 GPU + 1 FPGA)
ART
  ART on GPU is slow
  FPGA can accelerate
    in pipelined manner
oneAPI vs CUDA+OpenCL
  The execution time of oneAPI is increased by 1.5% => almost no overhead
no DPC++ version (undergoing)
Lower is better
R. Kashino, et al., “Multi-hetero Acceleration by GPU and FPGA for Astrophysics Simulation on oneAPI Environment”, HPC Asia 2022, Jan. 2022.

## Slide 43: Parallel ARGOT/CHARM with GPU+FPGA in oneAPI (CUDA+OpenCL)
Weak scaling with 2 nodes (2 GPUs + 2 FPGAs) (preliminary evaluation)
  largest mesh size on single FPGA is limited to 323
    1 node = 32x32x32 2 nodes = 64x32x32
Lower is better
0.89
0.13
2.05
0.16
・1 node
・GPU+FPGA achieves 6.8x faster than GPU-only
・2 nodes
・GPU+FPGA achieves12.8x faster than GPU-only
→ combining computation and communication in pipeline

## Slide 44: Performance ：MHOAT vs CUDA/OpenCL vs GPU-only (PPX single node: GPU: V100 + FPGA: Stratix10 size=32x32x32)
GPU (OpenACC or CUDA) vs CHARM (CUDA+OpenCL or MHOAT) ⇨ MHOAT is the best with 10x speed of OpenACC GPU
CHARM (CUDA+OpenCL vs MHOAT) ⇨ equal with OpenCL on ART method, but ARGOT method is better with OpenACC than CUDA
9.9x improved
1.4x improved
GPU only
CHARM (GPU+FPGA)

## Slide 45: Future work
Other killer applications : not found yet, but searching
  graph problem to apply FPGA for sort engine
  life science on quantum-level simulation where a number of functions run with small degree of parallelism
  other muti-physics simulation: climate, material science, ...
CIRCUS
  flow control and error detection
  applying parallel ART method on ARGOT code
Programming environment
  developing our own “CHARM-SYCL” now for easy modification and compact and portable version of SYCL based on CHARM concept
  MHOAT runtime to support CIRCUS and GPU-FPGA DMA for local data managemenet
Future
  single chip implementation with CPU/GPU/FPGA chiplets ?

## Slide 46: Summary
Toward Exa-scale era, homogeneous or single accelerator system will have limitation on application variation and scalability ⇨ from weak-scaling to strong-scaling
CCS, U. Tsukuba, is running a multi-hetero supercomputer named Cygnus under CHARM (Cooperative Heterogeneous Acceleration with Reconfigurable Multi-devices) concept by GPU+FPGA
Several supporting systems on FPGA and GPU coworking are developed including language solution toward high sustained performance of multi-physical simulations
MHOAT makes complicated programming much easier, but (CHARM-)SYCL is alternative to port existing code easier
Final goal of ARGOT = completely parallelized multi-node multi-hetero execution
Next Gen. HPC requires any of advanced technology, and FPGA will play an important role not just for the main engine for computation but also for compensation to many parts
Fully parallelized ARGOT/CHARM is coming soon for full size Cygnus
Call me if you want to use Cygnus with us!

## Slide 47: My Research Team
HPC Research Division at CCS, Univ. of Tsukuba
Architecture Team in High Performance Computing System Lab., Dept. of Computer Science, Univ. of Tsukuba
Astrophysics Research Division at CCS, Univ. of Tsukuba
Masayuki Umemura Kohji Yoshikawa
Ryohei Kobayashi Norihisa Fujita Yoshiki Yamaguchi Ryuta Tsunashima Ryuta Kashino

## Slide 48: THANK YOU !! Q?