## Slide 1: Enabling Multi-level Network Modeling in Structural Simulation Toolkit (SST) for Next-Generation HPC Network Design Space Exploration
Sai Chenna, Nalini Kumar, Leonardo Borges, Michael Steyer, Philippe Thierry, Maria Garzaran
HPC AI Software Solutions Engineer Intel Corporation
Notes: 1. Hello everyone, I’m Sai Chenna

## Slide 2: Outline
Introduction
Structural Simulation Toolkit (SST)
  Infrastructure for Network Modeling
Modeling Multi-level Networks in SST
  Building the topology
  Routing
Simulation Results
  Experimental Setup
  Motifs
  Analysis
Conclusions and Future Work

## Slide 3: Introduction
Increasing complexity of nodes & systems – leading to hierarchical networks
  E.g., Aurora, Grace-Hopper
Current modeling tools do not support multi-level network modeling
  Crucial for system co-design
Contribution:
  Adding support for multi-level network modeling in SST – parallel DES simulator
  Evaluation of our modeling approach on a two-level network system
Aurora Compute Node
Nvidia HGX Grace Hopper with NVLink Switch
Image courtesy: https://resources.nvidia.com/en-us-grace-cpu/nvidia-grace-hopper
Image courtesy: https://www.hpcwire.com/2020/11/17/intel-xe-hp-gpu-aurora-exascale-development/

## Slide 4: Structural Simulation Toolkit (SST)
Scalable, parallel DES* aimed to simulate large-scale systems
  Developed by Sandia National Laboratories (http://sst-simulator.org/ )
Key Features
  Scalability
    Uses MPI for graph partitioning to enable million + component simulation
  Multi-scale
    Provides both simple and detailed (~ cycle) models for memory, compute and network components
  Inter-operability
    Provides support to integrate third-party component models
      E.g., gem5, GPGPUSim etc..
  Open-source, modular and easily extendable
Key Components
  SST-Core: Simulation Backend
    Takes care of simulation startup, component partitioning, event passing etc..
  SST-Elements: Library containing detailed component models
    E.g.: Merlin (router), DRAMSim2 (memory), Ariel (CPU)
Image courtesy: Sandia National Laboratories
(http://sst-simulator.org/SSTPages/SSTTopDocTutorial/)
Integration Services
MPI and C++ Threads
Component
Component
Component
Component
SST Core
* Discrete Event Simulator

## Slide 5: SST: Infrastructure of Network Modeling
Ember
  Network traffic generator based on application communication patterns
  Packages HPC comm patterns as motifs
  Provides a collection of diverse HPC comm patterns
Firefly
  Interface b/w network driver (Ember) and the router models (Merlin)
  Provides packetization and byte movement engine
  Implementation of communication protocols
Merlin
  Provides low-level, flexible networking components to simulate high-speed networks
  Models flit-level movement, physical routing and delivery of packets
  Supported topologies – Fat-tree, Dragonfly, N-dimension Torus
SST Network modeling stack
Image courtesy: Sandia National Laboratories (https://www.osti.gov/servlets/purl/1513506)
Image courtesy: Sandia National Laboratories (https://www.osti.gov/servlets/purl/1513506)

## Slide 6: SST: Modeling Multi-level Networks
Multi-level networks(MLNs) provide higher path diversity in addition to low latency high BW communication
Modeling MLNs in SST requires two steps:
  Building the topology – instantiating router models and establishing SST links b/w routers and endpoints
  Routing – instantiate the topology sub-component class which determines the routing policy(ies)
Each network endpoint is connected to multiple network levels through a NIC module (switch)
Modular design:
  Each network level contains multiple network topologies
  Plug-n-play design to facilitate network DSE
Current implementation supports a three-level network
  Level – 0 (intra-node) network
  Level – 1 (inter-node) network
  Level – 2 (inter-cluster/inter-pod) network
Multi-level Network System

## Slide 7: Experimental Setup
Level 0 (intra-node) Topology | 
Topology | Fully connected (single switch)
Node size | 2,4,8,16,32
Link Bandwidth | 256 GB/s
Link Latency | 1 ns
Level 1 (inter-node) Topology | 
Topology | 2-D HyperX
Shape | (2,2),(2,4),(2,8),(2,16),(2,32),(4,2),(4,4),(4,8),(4,16),(8,2),(8,4),(8,8),(16,2),(16,4),(32,2)
Width | 1X1
Routing | Dimension Order Routing (DOR)
Link Bandwidth | 128 GB/s
Link Latency | 11 ns
Communication Pattern | 
Motifs | Halo2D, Halo3D, Sweep3D
Collective | Allgather, Allreduce, Alltoall
Iterations | 10
Message size | 1kB,2kB,4kB,16kB*,64kB
Performance metric | Performance metric
Simulated time = | 
Inter-node traffic = | Inter-node traffic =
Level 0 (intra-node) Topology | 
Topology | Fully connected (single switch)
Node size | 2,4,8,16,32
Link Bandwidth | 256 GB/s
Link Latency | 1 ns
Level 1 (inter-node) Topology | 
Topology | 2-D HyperX
Shape | (2,2),(2,4),(2,8),(2,16),(2,32),(4,2),(4,4),(4,8),(4,16),(8,2),(8,4),(8,8),(16,2),(16,4),(32,2)
Width | 1X1
Routing | Dimension Order Routing (DOR)
Link Bandwidth | 128 GB/s
Link Latency | 11 ns
Communication Pattern | 
Motifs | Halo2D, Halo3D, Sweep3D
Collective | Allgather, Allreduce, Alltoall
Iterations | 10
Message size | 1kB,2kB,4kB,16kB*,64kB
Performance metric | Performance metric
 | Inter-node traffic =
* Simulation results have been shown for 16kB message sizes

## Slide 8: Modeling Multi-level Networks: Two-level Network
Two-level network with 128 endpoints
Intra-node: Fully connected
Inter-node: 2-D HyperX (8,4)
Node-size: 4
Node-count: 32
endpoint
intra-node switch
inter-node switch
endpoint NIC

## Slide 9: Simulation results: Allreduce
Tree-based algorithm
  2LogP communication stages
Observation – Improved performance in two-level network
  Performance gain significant in case of denser nodes – more endpoints per node
  Collectives involve each process communicating with a group of processes – less spatial locality
  Not a significant reduction in inter-node traffic
Allreduce
Allreduce
Allreduce
Inter-node traffic
Results have been estimated or simulated

## Slide 10: Simulation results: Alltoall
P-1 communication stages
Observation – Improved performance in two-level network
  Performance gain significant in case of denser nodes – more endpoints per node
  Collectives involve each process communicating with a group of processes – less spatial locality
  Not a significant reduction in inter-node traffic
Alltoall
Alltoall
Alltoall
Inter-node traffic
Results have been estimated or simulated

## Slide 11: Simulation results: Allgather
LogP communication stages
Observation – Improved performance in two-level network
  Performance gain significant in case of denser nodes – more endpoints per node
  Collectives involve each process communicating with a group of processes – less spatial locality
  Not a significant reduction in inter-node traffic
Allgather
Allgather
Allgather
Results have been estimated or simulated
Inter-node traffic

## Slide 12: Simulation results: Halo2D
Models a 2D Halo exchange
Near neighbor communication
  Uses Blocking Send/Recv pair
Observation – Improved performance in two-level network
  Performance gain significant in case of denser nodes – more endpoints per node
  Inter-node traffic accounts only for 20% in case of 32 endpoint-node
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Halo2D communication
Inter-node traffic
Results have been estimated or simulated
Halo2D
Halo2D

## Slide 13: Simulation results: Halo3D
Models a 3D blocking Halo exchange
Near neighbor communication
  Uses Irecv/Send pair
Observation – Improved performance in two-level network
  Performance gain significant in case of denser nodes – more endpoints per node
  Inter-node traffic accounts only for 20% in case of 32 endpoint-node
Halo3D communication
Inter-node traffic
Results have been estimated or simulated
Halo3D
Halo3D

## Slide 14: Simulation results: Sweep3D
Models a 3D sweep communication from all 8 vertices
Each processor sends a slice of stencil data to its immediate neighbors – creating a wavefront type of communication
  Stresses the network latency
  Majority of processors have to wait a long time to receive the stencil data
Near neighbor communication
  Blocking Send/Recv pair
Observation – Improved performance in two-level network
  Performance gain significant in case of denser nodes – more endpoints per node
  Inter-node traffic accounts only for 20% in case of 32 endpoint-node
Sweep3D
Sweep3D
Inter-node traffic
Results have been estimated or simulated
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Sweep3D communication

## Slide 15: Conclusions and Future Work
Current and Future systems are becoming increasingly complex – leading to hierarchical networks
  Modeling is crucial to study the network co-design
We included support for modeling multi-level networks in SST – a PDES large-scale system simulator
We evaluated our modeling framework on a
  Two-level network system containing 128 network endpoints
  3 HPC motifs – Halo2D/3D and Sweep3D ; 3 Collectives: Allreduce, Allgather, Alltoall.
We quantified the performance impact of the node size, topology and comm patterns on both the intra-node and inter-node traffic.
Using a fully connected network at an intra-node level resulted in a drop of :
  80% in inter-node traffic for near-neighbor comm patterns (Halo2D/3D, Sweep3D)
  20% in inter-node traffic for MPI Collectives (Allgather, Allreduce, Alltoall)
Going forward, we would like to include:
  Support for multiple topologies
  Adaptive routing policies
  Trace-driven simulations.

## Slide 16: Legal Notices and Disclaimers
Intel technologies may require enabled hardware, software or service activation.
No product or component can be absolutely secure.
Your costs and results may vary.
Configurations:
Structural Simulation Toolkit version: 12.0.1 (http://sst-simulator.org/SSTPages/SSTBuildAndInstall_older_downloads/ ); modified to include support for multi-level networks. The modified simulator code is not yet publicly available.
© Intel Corporation. Intel, the Intel logo, and other Intel marks are trademarks of Intel Corporation or its subsidiaries. Other names and brands may be claimed as the property of others.

## Slide 17
Thank You!